## Slide 1
Prof Dr Joyanta Kumar Roy, PhD
Dumkal Institute of Engineering & Technology Dumkal, Murshidabad West Bengal, India
Wireless Sensor Network

## Slide 2: Sensor…?
Sensing element
Analog signal.(mA, V)
Analog Processing circuits
Digitizer (A/D)
Digital data (Serial
/ Parallel)
Physical parameter
Sensor Classification
Sensor
Analog
Wired
Wireless
Digital
Wired
Wireless

## Slide 3: Sensors for Smart Environments
MEASUREMENT FOR WIRELESS SENSOR NETWORK |  | 
 | MEASURANDS | TRANSDUCTION PRINCIPLE
PHYSICAL PROPERTIES | PRESSURE | PIEZO RESISTIVE, CAPACITIVE
 | TEMPERATURE | THERMISTOR, THERMOMECHANICAL, THERMOCOUPLE, RTD
 | HUMIDITY | RESISTIVE, CAPACITIVE
 | FLOW | PRESSURE CHANGE, THERMISTOR
MOTION PROPERTIES | POSITION | ELEC.MAG.,GPS,CONTACT SENSOR
 | VELOCITY | DOPPLER, HALL EFFECT,OPTOELECTRONICS
 | ANGULAR VELOCITY | OPTICAL ENCODER
 | ACCELERATION | PIEZO RESISTIVE, PIEZO ELECTRIC, OPTICAL FIBER

## Slide 4: Sensors for Smart Environments…..contd.
MEASUREMENT FOR WIRELESS SENSOR NETWORK |  | 
 | MEASURANDS | TRANSDUCTION PRINCIPLE
CONTACT PROPERTIES | STARIN | PIEZO RESISTIVE
 | FORCE | PIEZO ELECTRIC, PIEZO RESISTIVE
 | TORQUE | PIEZO RESISTIVE, OPTO-ELECTRONIC,
 | SLIP | DUAL TORQUE
 | VIBRATION | PIEZORESISTIVE, PIEZO-ELECTRIC, OPTICAL FIBER, ULTRASOUND
PRESENCE | TACTILE / CONTACT | CONTACT SWITCH / CAPACITANCE
 | PROXIMITY | HALL EFFECT, CAPACITANCE, MAGNETIC, SEISMIC, ACCOUSTIC RF
 | DISTANCE / RANGE | EMAG, SONAR, RADAR, TUNNELING
 | MOTION | EMAG,IR, ACCOUSTIC, SEISMIC

## Slide 5: Sensors for Smart Environments…..contd.
MEASUREMENT FOR WIRELESS SENSOR NETWORK |  | 
 | MEASURANDS | TRANSDUCTION PRINCIPLE
BIO-CHEMICAL | BIO CHEMICAL AGENT | BIO CHEMICAL TRANSDUCTION
IDENTIFICATION | PERSONAL FEATURES | VISION
 | PERSONAL ID | FINGER PRINT RETINAL SCAN VOICE HEAT PLUME

## Slide 6: WIRELESS SENSOR DOMAIN
The emerging domain of wireless sensor networks has yielded devices with a wide range of computation, communication, and sensing capabilities. These range from relatively powerful systems with PC-class processors and high-bandwidth wireless interfaces (e.g. IEEE 802.11), to much smaller, low-power nodes consisting of simple embedded microcontrollers and low-bandwidth radios operating in the 433 or 916 MHz ISM bands. Other wireless technologies, such as IEEE 802.15.4 (Zigbee), Bluetooth, and long-distance cellular have been investigated for sensor networks as well.

## Slide 7: WIRELESS SENSOR REQUIRMENT
Wireless sensor networks are typically battery-powered and therefore have a fixed energy budget to meet a given application lifetime. Moreover, the energy cost to transmit even small amounts of data greatly dominates that of computation . Therefore, it is often necessary for sensors to expend significant CPU cycles to perform local compression, filtering, and aggregation of data in order to save communication overhead.

## Slide 8: MICA MOTE
Developed at UC Berkeley in collaboration with Intel Research
Device consists of an 8-bit Atmel ATMEGA 128L microcontroller, 132K of memory, 512K of nonvolatile flash memory
A 19.2 Kpbs radio operating in the 433 MHz or 916 MHz spectrum.
The device consumes approximately 25 mA with both the CPU and radio active.
limiting lifetime on 2 AA batteries to about 5-6 days without any power-saving techniques
Life time can be extended significantly, up to months or years, by selectively powering down the radio, CPU, and other peripherals and operating at low duty cycle.
Wide range of sensors, including light, temperature, magnetometers, accelerometers, humidity, and passive infrared, have been integrated with the MICA device.
The MICA node is programmed in NesC , a component-oriented variant of C, and uses the TinyOS operating system,

## Slide 9: Example Sensor Network Node
Small Form Factor
Battery Operated
Wireless Communication
and Adhoc Networking
Interface to Various Sensors
Programmable CPU
Low Power Low Throughput
TinyOS for Event Driven
Mica2 Mote – Designed by UC Berkeley, Manufactured by Crossbow

## Slide 10: WIRELESS SENSOR MOTE –MICA-2 (TYPICAL CONSTRUCTIONAL VIEW)

## Slide 11: WSN MOTES----Typical Dimension
Mica2 Mote – Designed by UC Berkeley, Manufactured by Crossbow

## Slide 12: Detailed view of architecture
Regular events mapped solely to EP and slaves
Micro Controller included for irregular events
Slaves provide application specific HW
All resource usage is explicit
Micro
Controller
Event Processor
System Bus
Interrupt
Power Ctrl
Addr/Data
SRAM
Sensors
Radio
Message Processor
Data Filter
Timer
Addr/Data

## Slide 13: Abstract view of architecture
Event
Processor
Radio
Transceiver
Sensors
Slave
Blocks
Shared
Memory
General Purpose
Microcontroller

## Slide 14: Key goals of architecture
Energy Efficiency
Flexibility/Programmability
WSN SYSTEM
General Purpose
CPU
Remove Software Overhead
ASIC
Retain Programmability
Event-driven computation
Hardware accelerators for power-efficiency
Exploit regular operations
Optimize for sensor net workloads
Modular design
Fine-grain power management
Notes: asderftgyhujki

## Slide 15: Overview
Wireless sensor networks (WSN) are constrained by energy consumption
  Goal: Average power consumption <100 µW enables energy scavenging methods
Architectural approach:
  Holistic approach
  Event-driven architecture
  Modular hardware accelerators
  Fine-grain power management
In the implementation phase

## Slide 16: Energy is the primary limitation
CPU Mode | Current @3V |  | Radio Mode | Current @3V
Active | 8.0 mA |  | Receive | 7.0 mA
Idle | 3.2 mA |  | Transmit Min Power | 3.7 mA
Standby | 216 µA |  | Transmit Max Power | 21.5 mA
Power-save | 110 µA |  | Sensor Board | 0.7 mA
Mica2 Power Consumption Measured by component
Not the complete picture, how is power consumed in an application?
V. Shnayder, M. Hempstead, B. Chen, G. Werner-Allen, M. Welsh. Simulating the Power Consumption of Large-Scale Sensor Network Applications. (SenSys'04).

## Slide 17: Regular Application Behavior
Timer
Interrupt
Collect Sensor
Data
Prepare
Message
Send Radio
Message
Sense and Transmit
Message
Arrives
Decode
Message
Search Routing
Table
Resend Radio
Message
Receive and Forward
Abstract View
Example - GDI
Every 5 min
Burrow Occupancy
- infrared
- humidity
- Pack data in packet
- Calculate checksum
- wait for acknowledgement

## Slide 18
  Star
  Ring
  Bus
  Mesh
  Fully Connected
  Tree
  Basic Network Topologies
    ring
SELF HEALING NETWORK
NETWORK TOPOLOGIES

## Slide 19: Sample Application Space
Monitoring Apps
  Structural/Earthquake/Weather/Habitat monitoring
  Building/Border/Battlefield detection
  Road/traffic monitoring
Medical Apps
  Long-term health monitoring
  Untethered Pulseox Sensors
Business Applications
  Supply Chain Management
  Expired/Damaged Goods Tracking
  Automatic Checkout Systems

## Slide 20: GREAT DUCK ISLAND PROJECT
The Great Duck Island Habitat Monitoring project is a pilot application for the monitoring of migratory seabirds in the coast of Maine. In the spring of 2002, 32 wireless sensor nodes were deployed on Great Duck Island, Maine. These nodes monitor the microclimates in and around nesting burrows. At the end of the held season in November 2002, well over 1 million readings had been logged from the 32 motes deployed on the island and made available on the internet through the GDI Project Website .

## Slide 21: Example App: Great Duck Island
Great Duck Island (GDI), Maine - (UC Berkeley)
  Gather temp, humidity, IR readings from Leach's Storm Petrel burrows and weather station motes
  Determine occupancy of nests to understand migration patterns
  Total of 150 nodes deployed in 2003, over 650,000 observations taken
Performance Requirements are Low
  Samples taken and transmitted once every 5 min
Power consumption limited lifetime of deployment
R. Szewczyk et al. An Analysis of a Large Scale Habitat Monitoring Application. ACM Conference on Embedded Networked Sensor Systems (SenSys), 2004.
Single Hop Network
Multi-Hop Network

## Slide 22: WSN RECORDS DATA IN EVERY 5MIN & DATA AVAIALABLE FOR ANALYSIS IN GRAPHICAL FORM

## Slide 25
of nodes
new nodes, loss
Nodes moving,
Nodes are tiny
Limitations
Hardware
them low cost
Nodes die, make
Costs
nodes
Topology
Changing
Handle high density of
Scalability
Environment
Hostile
Authentication
Confidentiality,
Security ?
CONSTRAINT IN WIRELESS SENSOR NETWORKS
Survive and maintain
nodes
communication
Handle loss of
lifetime
Limited Tx,
Power
Fault Tolerance
Infrared

## Slide 26: THE END
THANK YOU